## Slide 1
Chapter 5
End-to-End Protocols
This work is licensed under a Creative Commons Attribution 4.0 License.

## Slide 2: Problem
How to turn this host-to-host packet delivery service into a process-to-process communication channel

## Slide 3: Chapter Outline
Simple Demultiplexer (UDP)
Reliable Byte Stream (TCP)
Remote Procedure Call (RPC)

## Slide 4: Chapter Goal
Understanding the demultipexing service
Discussing reliable byte-stream protocol
Understand how RPC works and how it relates to transport protocols

## Slide 5: End-to-end Protocols
Common properties that a transport protocol can be expected to provide
  Guarantees message delivery
  Delivers messages in the same order they were sent
  Delivers at most one copy of each message
  Supports arbitrarily large messages
  Supports synchronization between the sender and the receiver
  Allows the receiver to apply flow control to the sender
  Supports multiple application processes on each host

## Slide 6: End-to-end Protocols
Typical limitations of the network on which transport protocol will operate
  Drop messages
  Reorder messages
  Deliver duplicate copies of a given message
  Limit messages to some finite size
  Deliver messages after an arbitrarily long delay

## Slide 7: End-to-end Protocols
Challenge for Transport Protocols
  Develop algorithms that turn the less-than-desirable properties of the underlying network into the high level of service required by application programs

## Slide 8: Simple Demultiplexer (UDP)
Extends host-to-host delivery service of the underlying network into a process-to-process communication service
Adds a level of demultiplexing which allows multiple application processes on each host to share the network

## Slide 9: Simple Demultiplexer (UDP)
Format for UDP header (Note: length and checksum fields should be switched)

## Slide 10: Simple Demultiplexer (UDP)
UDP Message Queue

## Slide 11: Reliable Byte Stream (TCP)
In contrast to UDP, Transmission Control Protocol (TCP) offers the following services
  Reliable
  Connection oriented
  Byte-stream service

## Slide 12: Flow control VS Congestion control
Flow control involves preventing senders from overrunning the capacity of the receivers
Congestion control involves preventing too much data from being injected into the network, thereby causing switches or links to become overloaded

## Slide 13: End-to-end Issues
At the heart of TCP is the sliding window algorithm (discussed in Chapter 2)
As TCP runs over the Internet rather than a point-to-point link, the following issues need to be addressed by the sliding window algorithm
  TCP supports logical connections between processes that are running on two different computers in the Internet
  TCP connections are likely to have widely different RTT times
  Packets may get reordered in the Internet

## Slide 14: End-to-end Issues
  TCP needs a mechanism using which each side of a connection will learn what resources the other side is able to apply to the connection
  TCP needs a mechanism using which the sending side will learn the capacity of the network

## Slide 15: TCP Segment
TCP is a byte-oriented protocol, which means that the sender writes bytes into a TCP connection and the receiver reads bytes out of the TCP connection.
Although “byte stream” describes the service TCP offers to application processes, TCP does not, itself, transmit individual bytes over the Internet.

## Slide 16: TCP Segment
TCP on the source host buffers enough bytes from the sending process to fill a reasonably sized packet and then sends this packet to its peer on the destination host.
TCP on the destination host then empties the contents of the packet into a receive buffer, and the receiving process reads from this buffer at its leisure.
The packets exchanged between TCP peers are called segments.

## Slide 17: TCP Segment
How TCP manages a byte stream.

## Slide 18: TCP Header
TCP Header Format

## Slide 19: TCP Header
The SrcPort and DstPort fields identify the source and destination ports, respectively.
The Acknowledgment, SequenceNum, and AdvertisedWindow fields are all involved in TCP’s sliding window algorithm.
Because TCP is a byte-oriented protocol, each byte of data has a sequence number; the SequenceNum field contains the sequence number for the first byte of data carried in that segment.
The Acknowledgment and AdvertisedWindow fields carry information about the flow of data going in the other direction.

## Slide 20: TCP Header
The 6-bit Flags field is used to relay control information between TCP peers.
The possible flags include SYN, FIN, RESET, PUSH, URG, and ACK.
The SYN and FIN flags are used when establishing and terminating a TCP connection, respectively.
The ACK flag is set any time the Acknowledgment field is valid, implying that the receiver should pay attention to it.

## Slide 21: TCP Header
The URG flag signifies that this segment contains urgent data. When this flag is set, the UrgPtr field indicates where the nonurgent data contained in this segment begins.
The urgent data is contained at the front of the segment body, up to and including a value of UrgPtr bytes into the segment.
The PUSH flag signifies that the sender invoked the push operation, which indicates to the receiving side of TCP that it should notify the receiving process of this fact.
Finally, the RESET flag signifies that the receiver has become confused

## Slide 22: TCP Header
Finally, the RESET flag signifies that the receiver has become confused, it received a segment it did not expect to receive—and so wants to abort the connection.
Finally, the Checksum field is used in exactly the same way as for UDP—it is computed over the TCP header, the TCP data, and the pseudoheader, which is made up of the source address, destination address, and length fields from the IP header.

## Slide 23: Connection Establishment/Termination in TCP
Timeline for three-way handshake algorithm

## Slide 24: Sliding Window Revisited
TCP’s variant of the sliding window algorithm, which serves several purposes:
  (1) it guarantees the reliable delivery of data,
  (2) it ensures that data is delivered in order, and
  (3) it enforces flow control between the sender and the receiver.

## Slide 25: Sliding Window Revisited
Relationship between TCP send buffer (a) and receive buffer (b).

## Slide 26: TCP Sliding Window
Sending Side
  LastByteAcked ≤ LastByteSent
  LastByteSent ≤ LastByteWritten
Receiving Side
  LastByteRead < NextByteExpected
  NextByteExpected ≤ LastByteRcvd + 1

## Slide 27: TCP Flow Control
LastByteRcvd − LastByteRead ≤ MaxRcvBuffer
AdvertisedWindow = MaxRcvBuffer − ((NextByteExpected − 1) − LastByteRead)
LastByteSent − LastByteAcked ≤ AdvertisedWindow
EffectiveWindow = AdvertisedWindow − (LastByteSent − LastByteAcked)
LastByteWritten − LastByteAcked ≤ MaxSendBuffer
If the sending process tries to write y bytes to TCP, but
(LastByteWritten − LastByteAcked) + y > MaxSendBuffer
then TCP blocks the sending process and does not allow it to generate more data.

## Slide 28: Protecting against Wraparound
SequenceNum: 32 bits longs
AdvertisedWindow: 16 bits long
  TCP has satisfied the requirement of the sliding
  window algorithm that is the sequence number
  space be twice as big as the window size
  232 >> 2 × 216

## Slide 29: Protecting against Wraparound
Relevance of the 32-bit sequence number space
  The sequence number used on a given connection might wraparound
  A byte with sequence number x could be sent at one time, and then at a later time a second byte with the same sequence number x could be sent
  Packets cannot survive in the Internet for longer than the MSL
  MSL is set to 120 sec
  We need to make sure that the sequence number does not wrap around within a 120-second period of time
  Depends on how fast data can be transmitted over the Internet

## Slide 30: Protecting against Wraparound
Time until 32-bit sequence number space wraps around.

## Slide 31: Keeping the Pipe Full
16-bit AdvertisedWindow field must be big enough to allow the sender to keep the pipe full
Clearly the receiver is free not to open the window as large as the AdvertisedWindow field allows
If the receiver has enough buffer space
  The window needs to be opened far enough to allow a full
  delay × bandwidth product’s worth of data
  Assuming an RTT of 100 ms

## Slide 32: Keeping the Pipe Full
Required window size for 100-ms RTT.

## Slide 33: Triggering Transmission
How does TCP decide to transmit a segment?
  TCP supports a byte stream abstraction
  Application programs write bytes into streams
  It is up to TCP to decide that it has enough bytes to send a segment

## Slide 34: Triggering Transmission
What factors governs this decision
  Ignore flow control: window is wide open, as would be the case when the connection starts
  TCP has three mechanism to trigger the transmission of a segment
    1) TCP maintains a variable MSS and sends a segment as soon as it has collected MSS bytes from the sending process
      MSS is usually set to the size of the largest segment TCP can send without causing local IP to fragment.
      MSS: MTU of directly connected network – (TCP header + and IP header)
    2) Sending process has explicitly asked TCP to send it
      TCP supports push operation
    3) When a timer fires
      Resulting segment contains as many bytes as are currently buffered for transmission

## Slide 35: Silly Window Syndrome
If you think of a TCP stream as a conveyer belt with “full” containers (data segments) going in one direction and empty containers (ACKs) going in the reverse direction, then MSS-sized segments correspond to large containers and 1-byte segments correspond to very small containers.
If the sender aggressively fills an empty container as soon as it arrives, then any small container introduced into the system remains in the system indefinitely.
That is, it is immediately filled and emptied at each end, and never coalesced with adjacent containers to create larger containers.

## Slide 36: Silly Window Syndrome
Silly Window Syndrome

## Slide 37: Nagle’s Algorithm
If there is data to send but the window is open less than MSS, then we may want to wait some amount of time before sending the available data
But how long?
If we wait too long, then we hurt interactive applications like Telnet
If we don’t wait long enough, then we risk sending a bunch of tiny packets and falling into the silly window syndrome
  The solution is to introduce a timer and to transmit when the timer expires

## Slide 38: Nagle’s Algorithm
We could use a clock-based timer, for example one that fires every 100 ms
Nagle introduced an elegant self-clocking solution
Key Idea
  As long as TCP has any data in flight, the sender will eventually receive an ACK
  This ACK can be treated like a timer firing, triggering the transmission of more data

## Slide 39: Nagle’s Algorithm
When the application produces data to send
if both the available data and the window ≥ MSS
send a full segment
else
if there is unACKed data in flight
buffer the new data until an ACK arrives
else
send all the new data now

## Slide 40: Adaptive Retransmission
Original Algorithm
  Measure SampleRTT for each segment/ ACK pair
  Compute weighted average of RTT
    EstRTT = a x EstRTT + (1 - a )x SampleRTT
    a between 0.8 and 0.9
  Set timeout based on EstRTT
    TimeOut = 2 x EstRTT

## Slide 41: Original Algorithm
Problem
  ACK does not really acknowledge a transmission
    It actually acknowledges the receipt of data
  When a segment is retransmitted and then an ACK arrives at the sender
    It is impossible to decide if this ACK should be associated with the first or the second transmission for calculating RTTs

## Slide 42: Karn/Partridge Algorithm
Associating the ACK with (a) original transmission versus (b) retransmission

## Slide 43: Karn/Partridge Algorithm
Do not sample RTT when retransmitting
Double timeout after each retransmission

## Slide 44: Karn/Partridge Algorithm
Karn-Partridge algorithm was an improvement over the original approach, but it does not eliminate congestion
We need to understand how timeout is related to congestion
  If you timeout too soon, you may unnecessarily retransmit a segment which adds load to the network

## Slide 45: Karn/Partridge Algorithm
Main problem with the original computation is that it does not take variance of Sample RTTs into consideration.
If the variance among Sample RTTs is small
  Then the Estimated RTT can be better trusted
  There is no need to multiply this by 2 to compute the timeout

## Slide 46: Karn/Partridge Algorithm
On the other hand, a large variance in the samples suggest that timeout value should not be tightly coupled to the Estimated RTT
Jacobson/Karels proposed a new scheme for TCP retransmission

## Slide 47: Jacobson/Karels Algorithm
Difference = SampleRTT − EstimatedRTT
EstimatedRTT = EstimatedRTT + ( delta× Difference)
Deviation = Deviation +delta (|Difference| − Deviation)
TimeOut = μ × EstimatedRTT + phi × Deviation
  where based on experience, μ is typically set to 1 and phi is set to 4. Thus, when the variance is small, TimeOut is close to EstimatedRTT; a large variance causes the deviation term to dominate the calculation.

## Slide 48: Remote Procedure Call (RPC)
While TCP and UDP are often viewed as the complete set of Transport layer protocols, neither exactly meets needs of RPC
There is no single RPC protocol, rather a set of mechanisms to allow requests and responses to be delivered reliably & address the differences in machine architecture at sender and receiver

## Slide 49: RPC Fundamentals
Message identification (to match request with response)
Fragmentation/reassembly
Reliability
Marshalling – discussed in later chapter

## Slide 50: Perspective
More and more services run over HTTPS
At some point the Internet becomes less an IP-based network and more an HTTP network
This is a new “narrow waist” in the Internet architecture
Less narrow than IP (includes more features like reliability and security)

## Slide 51: Summary
We have discussed how to convert host-to-host packet delivery service to process-to-process communication channel.
We have discussed UDP
We have discussed TCP
We have discussed RPC